## Slide 1
Vedic Dutta &
Zaid Ahmed Khan
PREDICTING RHEOLOGICAL PROPERTIES USING AI & ML

## Slide 2
CONTENT
01
02
EXISTING RESEARCH
OUR APPROACH

## Slide 3
EXISTING RESEARCH

## Slide 4
Elastic Properties :
The prediction of elastic properties represents a significant application area, particularly in materials engineering :
  Storage and loss moduli prediction using advanced neural networks, particularly for viscoelastic materials and magnetorheological systems ( Link )
  Young's modulus, shear modulus, and bulk modulus for various material systems including metals, rocks, and composite materials ( Link-1 , Link-2 )
Viscosity Properties :
Viscosity remains the most extensively studied rheological property using AI/ML approaches. :
  Dynamic and apparent viscosity for drilling fluids, enabling real-time monitoring and automated mud system control ( Link )
  Viscosity of specialized fluids such as ionic liquids, deep eutectic solvents, binary liquid mixtures, and lubricants ( Link )
  Shear-rate dependent viscosity for complex and non-Newtonian fluids ( Link )
OTHER EXISTING PAPERS

## Slide 5
OUR
APPROACH

## Slide 6
MOTIVATION
  The generalized Maxwell model (GMM) used in vCANNs captures complex viscoelastic behavior ( Lin
  However, it often uses a large number of branches, leading to high computational cost and overfitting.
  Our goal: replace GMM with a compact, interpretable, and efficient model that preserves performance within a specified tolerance.
  We achieve this by learning a sparse viscoelastic network composed of Maxwell and Kelvin–Voigt (KV) elements.

## Slide 7
  Represent the viscoelastic model as a learnable physical network on a fixed mxm grid.
  Each grid edge can host one of 4 types:
Spring (S), Dashpot (P), Maxwell (SP), or Null (∅)
  A neural network learns:
Where to place branches
What type each branch should be
What parameters (G′,G′′G', G''G′,G′′) they should have
  The final model approximates the GMM with far fewer components.
IDEA

## Slide 8
MODEL WORKFLOW
  Input: Strain invariants and features (same as vCANN)
  Teacher model: Use vCANN to produce full generalized Maxwell parameters
  Compression network:
    Predicts a grid of components and their types/parameters
    Outputs a structured viscoelastic network
  Loss:
    Match GMM response (accuracy)
    Penalize unnecessary branches (sparsity)
    Encourage locality of branches (structural consistency)

## Slide 9
  Define a fixed mxm template grid (e.g., m=100)
  Each edge between grid nodes can be:
    Spring (S): stores elastic energy
    Dashpot (P): dissipates energy
    Maxwell (SP): both
    Null (∅): inactive / trimmed after training
  Parameters G′G'G′, G′′G''G′′ are predicted for each non-null edge
  The structure forms a directed, interpretable network
GRID-BASED PARAMETRIZATION

## Slide 10
LOSS FUNCTION
  Fit loss: matches the compact model’s output with the GMM
  Sparsity loss: discourages extra branches
  Compactness loss: discourages scattered elements far from the grid origin

## Slide 11
POST PROCESSING
After processing, remove:
  All ∅ edges
  Disconnected components
  Keep only the minimal, connected subgraph that reproduces behavior
  Output: a symbolic, interpretable model with greatly reduced complexity

## Slide 12
KEY BENEFITS
  Model reduction: compact replacement of large GMMs
  Interpretability: physical structure can be visualized and analyzed
  Efficiency: fewer branches lead to faster simulations in finite element solvers
  Generalization: structure is dynamically adapted to each material’s characteristics
  Avoiding Overfitting : Use of combination of Kelvin-Vogit and Maxewell model can lead to smaller Network to predict the substance properties

## Slide 13
FOR YOUR ATTENTION
THANK YOU