## Slide 1
Vedic Dutta &
Zaid Ahmed Khan
PREDICTING RHEOLOGICAL PROPERTIES USING AI & ML

## Slide 2
CONTENT
01
02
WORK DONE
PAPER OVERVIEW
03
DATASET USED
04
EXPERIMENTS DONE

## Slide 3
WORK
DONE

## Slide 4
  DONE LITERATURE REVIEW OF PAPER
  CURATED STRESS, STRAIN DATA FROM INTERNET FOR VARIOUS MATERIALS AT VARIOUS TEMPERATURE
  UPDATED THE VCAN GITHUB REPOSITORY TO MAKE IT WORKING AND GENERATED OUTPUT FOR VARIOUS CONFIGURATION AND COMPARED WITH PROPERTIES OF MATERIAL AVAILABLE AT THE INTERNET
  GENERATED RESULTS WITH DIFFERENT ARRANGEMENTS OF SPRINGPOT ELEMENT AND COMPARED WITH PROPERTIES OF MATERIAL AVAILABLE AT THE INTERNET
WORK DONE

## Slide 5
PAPER OVERVIEW

## Slide 6
•Soft materials like gels, tissues, and polymers exhibit viscoelastic behavior.
•Traditional models use springs and dashpots, but fail to capture power-law responses.
•Fractional calculus introduces new models using non-integer derivatives.
•Many soft materials show stress/strain decay as σ(t) ∝ t^(-β)
•Traditional exponential decay (e.g., e^(-t)) is insufficient.
•Requires models that account for slow, memory-dependent behavior.
UNDERSTANDING MATERIAL BEHAVIOR

## Slide 7
• Springpot is a fractional-order element.
• Governing equation of springpot system :
THE SPRINGPOT: BRIDGING SPRING AND DASHPOT
• Here Cb generally referes to firmness of a material and Beta is the power exponent
• Models combine springpots with traditional elements.
• Efficient modeling with fewer parameters.

## Slide 8
DATASET
USED

## Slide 9
  Material & Source: Aluminum alloy 6061-T651, 9 lots from multiple manufacturers
  Temperatures: 6 levels → 20, 100, 150, 200, 250, 300 °C
  Key Features:
    High-quality dataset enabling study of variability in aluminum mechanical behavior
    Useful for uncertainty quantification, probabilistic modeling, fire resistance design (Eurocode 9)
  Public Access: Available via Mendeley Data → DOI: 10.17632/rd6jm9tyb6.1
STRESS–STRAIN DATA FOR ALUMINUM

## Slide 10
EXPERIMENTS DONE

## Slide 11
  Source: Experimental stress–strain field for aluminium
  Goal: Fit constitutive models that map strain history → stress response
  Preprocessing:
    Uniform time-step Δt (=3s) calculated from strain increments.
  Models Used & Fairness Comparison Criteria:
    Maxwell and Springpot elements (k branches each)
        Same number of branches k in both models.
        Same optimizer (scipy.optimize.curve_fit) and bounds on parameters.
        Same dataset, fitted on entire series (no data leakage issues).
        RMSE (root-mean-square error) computed over the full dataset.
MODELLING POWER: IMPLEMENTATION DETAILS

## Slide 12
MODELLING POWER: RESULTS

## Slide 13
MODELLING POWER: PARALLEL+SERIES (2 STACKS)

## Slide 14
MODELLING POWER: OBSERVATIONS
  RMSE comparison:
    Springpot consistently achieved lower RMSE than Maxwell for the same k.
    Both models’ RMSE remained non-increasing as k increased, but neither reached near-zero error within tested k range.
  Qualitative fit:
    Maxwell model’s predicted stress curves often lagged or over-smoothed certain features.
    Springpot handled intermediate viscoelastic slopes better, likely due to fractional-order flexibility.
  Implication:
    For this dataset, springpot elements are more efficient at capturing the material’s stress–strain relationship per branch, for this particular material, although pronounced difference was not observed.
    Neither model with limited k perfectly interpolates the experimental curve — additional branches or hybrid formulations might be necessary for exact match, justifying grid-like architecture. Introducing two stacked layers instead of a single layer reduced the average generalisation error for both models. However, this did not decisively make springpot superior — Maxwell remains competitive.

## Slide 15
  Young Modulus for this dataset : 55 GPa using true dataset
  Young Modulus for this using Predicted P11 of VCAN : 0.00186 GPa
VCAN OUTPUT FOR ALUMINIUM AT T=100C

## Slide 16
  Young Modulus for this dataset : 31.75 GPa using true dataset
  Young Modulus for this using Predicted P11 of VCAN : 0.00149 GPa
VCAN OUTPUT FOR ALUMINIUM AT T=300C

## Slide 17
FOR YOUR ATTENTION
THANK YOU